## Slide 1
Conditionals
Condition Codes
  CF Carry Flag (for unsigned)
  SF(NF) Sign / Negative Flag (for signed)
  ZF Zero Flag
  OF Overflow Flag (for signed)
Setting CC
Using CC

## Slide 2
%rip
Registers
CF
ZF
SF
OF
Information about currently executing program
  Temporary data ( %rax, … )
  Location of runtime stack ( %rsp )
  Location of current code control point ( %rip, … )
  Status of recent tests ( CF, ZF, SF, OF )
Processor State
%rsp
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp
Instruction pointer
Condition codes

## Slide 3
Condition Codes (Implicit Setting)
Implicitly set (think of it as side effect) by arithmetic operations
  Example: addq Src,Dest ↔ t = a+b
  ZF set if t == 0
  SF set if t < 0 (as signed)
  CF set if carry out from most significant bit (unsigned overflow)
  OF set if 2’s-complement (signed) overflow (a>0 && b>0 && t<0) || (a<0 && b<0 && t>=0)
Not set by leaq instruction

## Slide 4
Condition Codes (Explicit Setting)
cmpq Src2, Src1: Set Conditions by Arithmetic Compare
  cmpq b,a like computing a-b without setting destination
    subq src2, src1 : src1 = src1-src2; CC(src1)
    cmpq src2, src1 : CF(src1-src2)
  ZF set if a == b
  SF set if (a-b) < 0 (as signed)
  CF set if carry out from most significant bit (used for unsigned comparisons)
  OF set if two’s-complement (signed) overflow (a>0 && b<0 && (a-b)<0) || (a<0 && b>0 && (a-b)>0)

## Slide 5
Condition Codes (Explicit Setting)
testq Src2, Src1: Set Conditions by Logical Test
  testq b,a like computing a&b without setting destination
    andq src2, src1 : src1 = src1&src2; CC(src1)
    testq src2, src1 : CC(src1&src2)
  Sets condition codes based on value of Src1 & Src2
  Typical use case: one operand is a mask
  ZF set when a&b == 0
  SF set when a&b < 0

## Slide 6
Reading Condition Codes
setX instructions
  Set a byte-size destination to 0 or 1 based on combinations of condition codes
  Does not alter remaining 7 bytes
SetX | Condition | Description
sete | ZF | Equal / Zero
setne | ~ZF | Not Equal / Not Zero
sets | SF | Negative
setns | ~SF | Nonnegative
setg | ~(SF^OF)&~ZF | Greater (Signed)
setge | ~(SF^OF) | Greater or Equal (Signed)
setl | (SF^OF) | Less (Signed)
setle | (SF^OF)¦ZF | Less or Equal (Signed)
seta | ~CF&~ZF | Above (unsigned)
setb | CF | Below (unsigned)

## Slide 7
cmpq %rsi, %rdi # Compare x and y (x-y)
  setg %al # Set %al when x > y
  movzbl %al, %rax # Zero rest of %rax
ret
Reading Condition Codes
setX instructions:
  Set single byte based on combination of condition codes
Uses one of the byte registers (%al, %ah, %bl, …)
  Does not alter remaining bytes in the extended register
  Typically use movzbl to finish job
    32-bit instructions also set upper 32 bits to 0
int gt (long x, long y)
{
return x > y;
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value

## Slide 8
Jumping
jX Instructions
  Jump to different part of code depending on condition codes
jX | Condition | Description
jmp |  | Unconditional
je | ZF | Equal / Zero
jne | ~ZF | Not Equal / Not Zero
js | SF | Negative
jns | ~SF | Nonnegative
jg | ~(SF^OF)&~ZF | Greater (Signed)
jge | ~(SF^OF) | Greater or Equal (Signed)
jl | (SF^OF) | Less (Signed)
jle | (SF^OF)¦ZF | Less or Equal (Signed)
ja | ~CF&~ZF | Above (unsigned)
jb | CF | Below (unsigned)

## Slide 9
if (t)
then-statement;
else
else-statement;
t = test_expr;
if (!t)
goto false;
do then-statement;
goto done;
false:
do else-statement;
done:
int goto_max(int x, int y)
{
int rval = y;
int ok = (x <= y);
if (ok)
goto done;
rval = x;
done:
return rval;
}
int max(int x, int y)
{
if (x > y)
return x;
else
return y;
}
Conditional Branch

## Slide 10
Carnegie Mellon
Expressing with Goto Code
long absdiff(long x, long y)
{
long result;
if (x > y) {
result = x-y;
return result;
} else {
result = y-x;
return result;
}
}
C allows goto statement
Jump to position designated by label
long absdiff_j(long x, long y)
{
long result;
CMP(x, y);
if (LT) goto Else;
result = x-y;
return result;
Else:
result = y-x;
return result;
}

## Slide 11
Carnegie Mellon
Conditional Branch Example
absdiff:
# %rdi = x; %rsi = y
cmpq %rsi, %rdi # x:y
jle .L4
movq %rdi, %rax
subq %rsi, %rax
ret
.L4: # x <= y
movq %rsi, %rax
subq %rdi, %rax
ret
Generation -- on mercury.cs.uml.edu
  > gcc –Og -S control.c
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value
long absdiff_j(long x, long y)
{
long result;
CMP(x, y);
if (LT) goto Else;
result = x-y;
return result;
Else:
result = y-x;
return result;
}

## Slide 12
Carnegie Mellon
x86 vs. MIPS
x86
absdiff:
# %rdi = x; %rsi = y
# cmpq y, x (x <= y)
cmpq %rsi, %rdi #<=
jle .L4
# if (%rdi <= %rsi) (x-y)
movq %rdi, %rax
subq %rsi, %rax
ret
.L4: # x <= y
movq %rsi, %rax
subq %rdi, %rax
ret
In C: if (x > y)
In pseudo-C: if (x <= y) goto else
Fake MIPS with x86 registers
absdiff:
# %rdi = x; %rsi = y
# ble x<=y, else
ble %rdi, %rsi, else
# if (%rdi <= %rsi)
move %rax, %rdi
sub %rax, %rax,%rsi
ret
else: # x <= y
move %rax, %rsi
sub %rax, %rax, %rdi
ret

## Slide 13
Carnegie Mellon
C Code
val = Test ? Then_Expr : Else_Expr;
Goto Version
ntest = !Test;
if (ntest) goto Else;
val = Then_Expr;
goto Done;
Else:
val = Else_Expr;
Done:
. . .
General Conditional Expression Translation (Using Branches)
  Create separate code regions for then & else expressions
  Execute appropriate one
val = x>y ? x-y : y-x;

## Slide 14
Carnegie Mellon
C Code
val = Test
? Then_Expr
: Else_Expr;
Goto Version
result = Then_Expr;
eval = Else_Expr;
nt = !Test;
if (nt) result = eval;
return result;
Using Conditional Moves
Conditional Move Instructions
  Instruction supports:
    if (Test) Dest  Src
  Supported in post-1995 x86 processors
  GCC tries to use them
    But only when known to be safe
Why?
  Branches are very disruptive to instruction flow through pipelines
  Conditional moves do not require control transfer

## Slide 15
Carnegie Mellon
Conditional Move Example
absdiff: # x = rdi, y = rsi
movq %rdi, %rax # rax = x
subq %rsi, %rax # result = x-y
movq %rsi, %rdx # rdx = y
subq %rdi, %rdx # eval = y-x
cmpq %rsi, %rdi # x:y
cmovle %rdx, %rax # if x<=y, result = rdx
ret
long absdiff
(long x, long y)
{
long result;
result = x>y ? x-y : y-x;
return result;
}
long absdiff(long x, long y)
{
long result;
if (x > y)
result = x-y;
else
result = y-x;
return result;
}

## Slide 16
Carnegie Mellon
Expensive Computations
Bad Cases for Conditional Move
Both values get computed
Only makes sense when computations are very simple
val = Test(x) ? Hard1(x) : Hard2(x);
Risky Computations
Both values get computed
May have undesirable behavior
val = p ? *p : 0;
Computations with side effects
Both values get computed
Must be side-effect free
val = x > 0 ? x*=7 : x+=3;

## Slide 17
Carnegie Mellon
Loops
Do while
do
Body
while (Test);
Goto Version
loop:
Body
if (Test) goto loop;
movl $0, %eax # result = 0
.L2: #loop:
movq %rdi, %rdx
andl $1, %edx # t = x & 0x1
addq %rdx, %rax # result += t
shrq %rdi # x >>= 1
jne .L2 # if (x) goto loop
ret
long pcount_goto
(unsigned long x)
{
long result = 0;
loop:
result += x & 0x1;
x >>= 1;
if(x) goto loop;
return result;
}

## Slide 18
Carnegie Mellon
Loops
While
while (Test)
Body
Goto Version
goto test;
loop:
Body
test:
if (Test) goto loop;
done:
“Jump-to-middle” translation
Used with -Og
loop:
if (!Test) goto done;
Body
goto loop;
done:
“Do-while” conversion
Used with –O1

## Slide 19
Carnegie Mellon
“For” Loop  While Loop
for (Init; Test; Update )
Body
For Version
Init;
while (Test ) {
Body
Update;
}
While Version
Init;
loop:
if (!Test)goto done;
Body
Update;
goto loop;
done:

## Slide 20
Carnegie Mellon
Switch Statement
Multiple case labels
  Here: 5 & 6
Fall through cases
  Here: 2
Missing cases
  Here: 4
long switch_eg
(long x, long y, long z)
{
long w = 1;
switch(x) {
case 1:
w = y*z;
break;
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
case 5:
case 6:
w -= z;
break;
default:
w = 2;
}
return w;
}

## Slide 21
Carnegie Mellon
Jump Table Structure
Code Block
0
Targ0:
Code Block
1
Targ1:
Code Block
2
Targ2:
Code Block
n–1
Targn-1:
•
•
•
Targ0
Targ1
Targ2
Targn-1
•
•
•
JTab:
goto *JTab[x];
switch(x) {
case val_0:
Block 0
case val_1:
Block 1
• • •
case val_n-1:
Block n–1
}
Switch Form
Translation (Extended C)
Jump Table
Jump Targets
goto Targ0
goto Targ1

## Slide 22
Carnegie Mellon
Switch Statement Example
long switch_eg(long x, long y, long z)
{
long w = 1;
switch(x) {
. . .
}
return w;
}
Indirect jump
Jump table
.section .rodata
.align 8
.L4:
.quad .L8 # x = 0
.quad .L3 # x = 1
.quad .L5 # x = 2
.quad .L9 # x = 3
.quad .L8 # x = 4
.quad .L7 # x = 5
.quad .L7 # x = 6
Setup:
switch_eg:
movq %rdx, %rcx
cmpq $6, %rdi # x:6
ja .L8 # Use default
jmp *.L4(,%rdi,8) # goto *JTab[x]

## Slide 23
Carnegie Mellon
Switch Statement Example
Setup:
long switch_eg(long x, long y, long z)
{
long w = 1;
switch(x) {
. . .
}
return w;
}
switch_eg:
movq %rdx, %rcx
cmpq $6, %rdi # x:6
ja .L8
jmp *.L4(,%rdi,8)
What range of values take the default jump?
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | Return value

## Slide 24
Carnegie Mellon
Assembly Setup Explanation
Table Structure
  Each target requires 8 bytes
  Base address at .L4
Jumping
  Direct: jmp .L8
  Jump exit is denoted by label .L8
  Indirect: jmp *.L4(,%rdi,8)
  Start of jump table: .L4
  Must scale by factor of 8 (addresses are 8 bytes)
  Fetch target from effective Address .L4 + x*8
    Only for 0 ≤ x ≤ 6
Jump table
.section .rodata
.align 8
.L4:
.quad .L8 # x = 0
.quad .L3 # x = 1
.quad .L5 # x = 2
.quad .L9 # x = 3
.quad .L8 # x = 4
.quad .L7 # x = 5
.quad .L7 # x = 6

## Slide 25
.section .rodata
.align 8
.L4:
.quad .L8 # x = 0
.quad .L3 # x = 1
.quad .L5 # x = 2
.quad .L9 # x = 3
.quad .L8 # x = 4
.quad .L7 # x = 5
.quad .L7 # x = 6
Carnegie Mellon
Jump Table
Jump table
switch(x) {
case 1: // .L3
w = y*z;
break;
case 2: // .L5
w = y/z;
/* Fall Through */
case 3: // .L9
w += z;
break;
case 5:
case 6: // .L7
w -= z;
break;
default: // .L8
w = 2;
}

## Slide 26
Carnegie Mellon
Code Blocks (x == 1)
.L3:
movq %rsi, %rax # y
imulq %rdx, %rax # y*z
ret
switch(x) {
case 1: // .L3
w = y*z;
break;
. . .
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | Return value

## Slide 27
Carnegie Mellon
Handling Fall-Through
long w = 1;
. . .
switch(x) {
. . .
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
. . .
}
case 3:
w = 1;
case 2:
w = y/z;
goto merge;
merge:
w += z;

## Slide 28
Carnegie Mellon
Code Blocks (x == 2, x == 3)
.L5: # Case 2
movq %rsi, %rax
cqto
idivq %rcx # y/z
jmp .L6 # goto merge
.L9: # Case 3
movl $1, %eax # w = 1
.L6: # merge:
addq %rcx, %rax # w += z
ret
long w = 1;
. . .
switch(x) {
. . .
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
. . .
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rcx | Argument z
%rax | Return value

## Slide 29
Carnegie Mellon
Code Blocks (x == 5, x == 6, default)
.L7: # Case 5,6
movl $1, %eax # w = 1
subq %rcx, %rax # w -= z
ret
.L8: # Default:
movl $2, %eax # 2
ret
switch(x) {
. . .
case 5: // .L7
case 6: // .L7
w -= z;
break;
default: // .L8
w = 2;
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rcx | Argument z
%rax | Return value

## Slide 30
Carnegie Mellon
Summary
C Control
  if-then-else
  do-while
  while, for
  switch
Assembler Control
  Conditional jump
  Conditional move
  Indirect jump (via jump tables)
Standard Techniques
  Loops converted to do-while or jump-to-middle form
  Dense switch statements use jump tables
  Sparse switch statements use decision trees (if-elseif-elseif-else)